## Slide 1: Best Practices and Best Available Technology for Prevention and Mitigation of Impacts of Hydrocarbons Within Wetlands
Paul R. Krause, Ph.D.
Knowledge Management Program
Sensitive Ecosystem Workshop Bogota, Colombia November 2012

## Slide 2: Best Practices and Technologies
  There are three important aspects of a successful oil and gas exploration program in and near wetlands
  Prevention – To prevent habitat degradation it is vital to understand the type and level of impact form activities
  Mitigation – Not all impacts can be avoided, but good mitigation practices will lessen the net impact of activities
  Monitoring – Development of a strong monitoring program both before and after development activities will provide solid evidence and documentation of impact

## Slide 3: Prevention
The world’s leading sustainability consultancy

## Slide 4: Prevention Practices – Impact Analysis
  The key to successful prevention is a good understanding of the expected project impacts. This is accomplished through Impact Analysis
  Environmental, Social, and Health Impact Assessment (ESHIA)
    Global standard practice for large capital projects such as O&G exploration and production projects.
      Addresses impacts from the project on:
        Environmental – ecology, biodiversity, ecosystem services
        Social –human populations, economy, project integrations
        Health –human health
  Environmental Impact Assessment (EIA)
    US National Standard under the National Environmental Policy Act (NEPA)
    US State-wide regulations
      California Environmental Quality Act (CEQA)

## Slide 5: Prevention Practices – Plans
  Another key aspect is the development of comprehensive plans for projects
  Spill Planning
    Development of a National Response System
      US Coast Guard is lead agency in the US
    Development Regional Response Plans
      Mapping of Resources at Risk (RAR)
        Sensitive ecological areas
        Important economic areas
      Tactical Response Plans (TRP)
        Boom placement
        Equipment locations
    Project-specific Plans
      Modelling of spill scenarios for all projects

## Slide 6: Prevention Practices – Plans
  Project-Specific Plans
    Spill Response Plan
      Modelling of spill scenarios
      Implementation of TAP
    Land Use Plan
      Erosion control
      Effective road and infrastructure path citing
      Designated project avoidance areas
    Water Use Plan
      Project water needs
      Population water needs
      Changes to natural water pattern
      Waste water handling
    Health and Safety Plans

## Slide 7: Prevention Technologies
  Spill Modelling
    Conducted over several likely spill scenarios under project conditions
    Results should include concentration ranges expected throughout the water column (i.e., 3-D Models)
    Use high-resolution models
      GEMSS
      NOAA
  Resources at Risk Mapping
    Conducted prior to project start
    Part of comprehensive National Plan
    GIS/Interactive based maps

## Slide 8: Prevention Technologies
  Tactical Response Plans
    Location of pre-positioned equipment
      Oil Boom
      Dispersant
      Decontamination equipment
      Waste handling materials
    Response contacts
      Regulatory
      Project Owner
      Consultant Base
    Shoreline Clean up and Assessment Teams
  Oil Spill Conferences
    Clean Conferences – Pacific, Caribbean, Gulf of Mexico www.cleanpacific.org www.cleancaribbean.org www.cleangulf.org
    International Oil Spill Conference www.iosc.org

## Slide 9: Mitigation
The world’s leading sustainability consultancy

## Slide 10: Mitigation Practices – Restoration
  All impacts are not avoidable.
  Mitigation Measures are designed to lessen or offset the impact of project activities that cannot be avoided
  Restoration
    Replaces lost habitat or service loss
      Can be at the project site or offsite
      Generally in a 1:1 or higher ratio
      Does not have to be like-for-like restoration but should provide the same level of service
        Habitat Equivalency Analysis (HEA)
        Resource Equivalency Analysis (REA)
      Opportunity for Joint Industry/Agency/NGO project partnerships.
        Coastal America – Wetlands Projects
        www.coastalamerica.gov

## Slide 11: Mitigation Practices – Mitigation Bank
  Mitigation Banking
    Used to offset the impacts to a public resource after impacts are determined.
    Mitigation bank is set up by resource agencies to sell “mitigation credits” to developers whose projects will impact the resource
    EXAMPLE: Wetlands impacted by O&G Exploration
      Proposed project would impact 100 Hectares (ha) of wetland
      Agency would set up mitigation bank and sell mitigation credits in units of 1 ha
      Developer needs to offset the of impact of a different project
      Developer would then buy mitigation credits rather than do the restoration work
      The number of mitigation credits would be determined by consultation with the agency.
      Agency would use mitigation bank funds to restore the 100 ha wetland impact after all funds were in place through the mitigation bank.
    This has been used extensively in the US by Federal and State Agencies to provide restoration mitigation under a variety of circumstances

## Slide 12: Mitigation Technology – HEA
  Habitat Equivalency Analysis
  Developed by NOAA to determine the appropriate size of compensatory restoration (CR) projects for Natural Resource Damage (NRD) Assessments
  Habitats provide services to other natural resources (e.g., wetlands provide food and protection for juvenile fish)
    “Losses” occur when services are reduced by injuries or destructive activities
    “Gains” occur when services are increased by restoration or enhancement actions
  Estimates net environmental impacts, accounting for both service losses and gains
  Includes both short-term and long-term service gains and losses

## Slide 13: Mitigation Technology – HEA
Measurement of Service Losses

## Slide 14: Mitigation Technology – HEA
Measurement of Service Gains

## Slide 15: Monitoring
The world’s leading sustainability consultancy

## Slide 16: Monitoring Practice – Understanding Baseline
  Knowing the baseline environmental conditions before a project begins is vital to being able to understand impacts.
  Key aspects of a good baseline study
    Impact and Control sites
      Focus on regional issues
    Multiple seasons
    Multiple stations within a site
    Broad array of sample types
      Chemical Hydrocarbon Fingerprint
        Sediment
        Water
      Biological
        Ecological
        Tissue

## Slide 17: Monitoring Technologies – LIDAR
  Light Detection and Ranging (LIDAR) is used to provide wide area data on elevation of wetlands.
  It penetrates shallow water bodies and provides general coverage estimates of plants.

## Slide 18: Conclusions
  Prevention activities will minimize impacts before they happen and will prevent damage if they do
    Impact Assessment
    Project and Response Planning
  Because all impacts cannot be avoided, mitigation measures will lessen the net impact
    Restoration
    Mitigation Banking
    HEA
  Monitoring activities and development of robust environmental baseline data will provide evidence of impact level and severity

## Slide 19: Effects on Wetland Function or Service
Any Questions?

## Slide 20
www.erm.com